| SPK-Z-GGS III GPS/GSM COMBINED STICKING ANTENNA In car sticking method GPS/GSM antenna To solve disadvantages of GPS signal receiving capability |
| --- |
| GSM Band PFrequency: 900MHZ、1800MHZ Gain: 3dB@900MHZ、2.5dB@1800MHZ PVSWR: ?2.0 Cable: RG-174U、3M、6M Connector: SMA、BNC、TNC、MCX、MMCX Physical specification Operating Temperature: -45℃～+85℃ PAnti-spray, anti-water splashing Installation: stick PDimension: 71mm×76.7mm×13.5mm(max) Weight: 50g(not include cable) Main function PCar GPS Alarm system PControl Movable objects | GPS Band Frequency: GPS L1(C/A) Gain: 30dB Noise figure: 1.4dB@1575.42MHZ±1.023MHz VSWR: 1.8:1 Bandwidth: 42MHZ@3dB Polarization: righ－hand circular Antenna elev pattern: ?4.0dB@±0°(Vertical) ?3.0dB@±30° ?4.0dB@±60° ?4.5dB@±90° ?3.0dB@±120° Voltage: 5±0.5VDC、3V±0.3VDC Power requirement: 16mA@5VDC Cable: RG-174U、3M、6M Connector: SMA、BNC、TNC、MCX、MMCX |